## Slide 1
ECE 420 Final Project Presentation
Electrical & Computer Engineering
By Ethan. Z & Eric. T
May 3rd 2024

## Slide 2
1. App operation overview
a. Introduction
b. User Interface
                2. System Designs
                a. System level algorithm
                b. System architecture
                3. Algorithms
                a. REPET
                b. Pitch correction
                4. Results & Feedback
                a. Demo
GRAINGER ENGINEERING
Table of content
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
App Operation Overview
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
Purpose & Function
The Main functionality of our app is to provide auto-tune feature, which adjusts the pitch of the user’s singing to a pre-processed or live-recorded soundtrack. Allowing users to enhance their vocal performance.
A key feature of the app is its ability to separate BGM and vocal components from any song captured via Android’s integrated microphone. This method allows individual component of the song to be analyzed and manipulated.
Algorithms Used
Repet for BGM/Vocal separation,
TD-PSOLA for Pitch Synthesis,
STFT/Autocorrelation for spectrum analysis.
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING

## Slide 5
Home Screen Target Song Screen Voice Synthesis Screen
GRAINGER ENGINEERING
User Interface
ELECTRICAL & COMPUTER ENGINEERING
Go to Voice Synthesis screen
Go to BGM/Vocal processing
screen
Go to Home Screen
Record the song and encode/ write to storage
Encode and write the processing result (BMG & Vocal) to storage
Play the vocal component
Play the BGM
Select source of target BGM
Record the song
Play the BGM
Encode and store the result
Play the Result

## Slide 6
System Designs
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
GRAINGER ENGINEERING
System level algorithm
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
All audio data are stored in storage in stead of loaded in the memory
The encoding and decoding of audio data is handled by ffmpeg in Java/Kotlin
The Front end passes decoded audio data (int16 array) to the C++ Processing Frames
GRAINGER ENGINEERING
System Architecture
ELECTRICAL & COMPUTER ENGINEERING
Front end
(JAVA/KOTLIN)
REPET
Processes
(C++)
Pitch Synthesis
Processes
(C++)
APK storage
Run time storage

## Slide 9
Algorithms
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
Purpose of REPET: REPET is specifically designed to identify and extract repeating musical structures from a mixed audio signal.
How It Works: The algorithm operates by exploiting the repetitive nature of the background music in most recorded songs. REPET identifies the repeating patterns by analyzing the audio signal's spectrogram and isolates the background track from non-repeating components like vocals.
GRAINGER ENGINEERING
REpeating Pattern Extraction Technique (REPET)
ELECTRICAL & COMPUTER ENGINEERING
Run time storage

## Slide 11
Partition: the User singing and the vocal component will be partitioned to segments with 1024 samples of width
Frequency analysis: Autocorrelation will be applied to each segment of vocal component to detect fundamental frequency and period
Pitch Synthesis: Each segment of the user singing would be match with a segment from the vocal track. The segment will then be pitch changed to match the frequency of respective vocal track
GRAINGER ENGINEERING
Pitch correction
ELECTRICAL & COMPUTER ENGINEERING
Run time storage

## Slide 12
Results & FeedBack
Demo/ Q&A
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING